## Slide 1: FALL DETECTION OF ELDERLY PEOPLE
School of Electronics Engineering
Prof. Abhijit Bhowmick
Project Guide
SIJO BABY MATHEWS - 14BEC0080
Final Review Presentation
Date of Presentation: 21/04/2018
B.Tech Electronics and Communication Engineering

## Slide 2: CONTENTS
Introduction
Literature Review
    Knowledge gained
    Gaps identified from literature
Objectives
Equipment and Technical Specification
Methodology
Results & Discussion
References
B.Tech Electronics and Communication Engineering – Final Review Presentation - SENSE

## Slide 3: Introduction
The major cause of injury and accidental deaths in old people is due to unexpected fall. According to recent statistics, majority of serious consequences are not due to direct fall but due to lack of immediate attention and treatment. Post-fall consequences can be reduced if relief personnel are alerted in time. Many modern old people prefer living alone independently after their children have grown up and leave home. It is so common that after a fall an elderly is unable to get up by themselves or contact someone for help. Thus, there is a need for an automated fall detection system such that he or she can summon help when they are unable to get up or is unconscious.
Many algorithm has already been developed but still it is difficult to differentiate real falls from certain activities such as sitting quickly, jumping which results in many false positives, as it uses accelerometer to detect fall with body orientation as ending position is not always horizontal. E.g. fall on stairs.
The fall detection algorithm can be developed is using both accelerometer and gyroscope reducing both false positives and false negatives, while improving fall detection accuracy. It notifies a concern person with SMS either automatic when fall occurs or with a panic button.
B.Tech Electronics and Communication Engineering – Final Review Presentation - SENSE

## Slide 4: Literature Review
Title of the paper | Journal & Year | Authors | Description | Remarks
"A wearable wireless fall detection system with accelerators" | 2011 IEEE International Conference | D. Chen, W. Feng, Y. Zhang, X. Li and T. Wang | DOI: 10.1109/ROBIO.2011.6181634 | Accelerometer to detect fall.
“Activity Analysis, Summarization, and Visualization for Indoor Human Activity Monitoring” | IEEE Transactions on Circuits and Systems for Video Technology ( Volume: 18, Issue: 11, Nov. 2008 | Zhongna Zhou, Xi Chen, Yu-Chia Chung, Zhihai He | DOI: 10.1109/TCSVT.2008.2005612 | Microsoft Kinect and cameras used for monitoring elderly while they are indoors.
"Risk factors for serious fall related injury in elderly women living at home." | Injury Prevention (2004): | Bergland, A., and TB Wyller. | doi:10.1136/ip.2003.004721 | risks faced by women after a fall which results in injury
B.Tech Electronics and Communication Engineering – Final Review Presentation - SENSE

## Slide 5: Literature Review
Title of the paper | Journal & Year | Authors | Description | Remarks
"Risk Factors in Falls Among the Elderly According to Extrinsic and Intrinsic Precipitating Causes." | European Journal of Epidemiology, 2000 | Bueno-Cavanillas, A.F. Padilla-Ruiz, J. J. Jiménez-Moleón | doi:10.1023/A:1007636531965 | Various risks factors that result in fall of old people.
"Evaluation of a threshold-based tri-axial accelerometer fall detection algorithm." | Gait & Posture (2007) | Bourke, A. K., J. V. O’Brien, and G. M. Lyons | doi:10.1016/j.gaitpost.2006.09.012 | Threshold value for fall detection was obtained from this research paper.
B.Tech Electronics and Communication Engineering – Final Review Presentation - SENSE

## Slide 6: Knowledge Gained from the Literature
32% of elderly people aged over 75 years have ever fallen at least once a year, and along with them, 24% have dangerously injured. Fall related injuries are the leading source of death and hospitalization surrounded by the elderly. Falls among older people become a major problem facing hospitals and nursing homes.
The need of support in the case of unconsciousness or extreme injury is the main reasons why elders leave the comfort and privacy of their own home to live in an assisted-care environment.
Visual monitoring using cameras and Microsoft Kinect to detect the fall is efficient method.
B.Tech Electronics and Communication Engineering – Final Review Presentation - SENSE

## Slide 7
Visual observation with some visual device which can observe the person continuously and then image analyser which can analyse the fall of the person and generate alarm. These systems use sensors deployed in the environment to detect falls. The main advantage of this system is the person does not need to wear any special device. The scope of this kind of device is limited to monitoring region (Majorly indoors) cannot be carried all the time with the person Information provided by device is quite accurate but such equipment will cost higher.
As for fall detection through an accelerometer, the scope of activity is relatively unrestricted; the device is easily attached to the human body, and the cost of system is low as compared to vision based method.
Gaps in the Literature
B.Tech Electronics and Communication Engineering – Final Review Presentation - SENSE

## Slide 8: Objectives
The main objectives of this work are:
(1) To design a fall detection system using low cost fall detector sensors,
(2) To develop an algorithm that can identify the body position of the elderly people whether it is in falling tendency, and
(3) To construct a system that can send an Emergency SMS to the contact person (e.g. next-of-kin or close relatives) stored in the system.
(4). To connect a pulse sensor and sent its value via SMS.
(5). GPS module to sent location as latitude and longitude via SMS.
B.Tech Electronics and Communication Engineering – Final Review Presentation - SENSE

## Slide 9: Objectives
B.Tech Electronics and Communication Engineering – Final Review Presentation - SENSE
Block representation of the model

## Slide 10: Equipment & Technical Specifications
B.Tech Electronics and Communication Engineering – Final Review Presentation - SENSE
SYSTEM REQUIREMENTS
• ARDUINO UNO
• ACCELEROMETER
• GPS
• GSM
PUSH BUTTON
PULSE SENSOR
SOFTWARE TOOLS
• ARDUINO IDE
• EMBEDDED C

## Slide 11: Methodology
During a fall, a person experiences a momentary freefall or reduction in acceleration, followed by a large spike in acceleration, then a change in orientation.
We see the algorithm checks to see if the acceleration magnitude (AM) breaks a set lower threshold. If this lower threshold is broken, the algorithm then checks to see if AM breaks a set upper threshold within 0.5s. If this upper threshold is broken, the algorithm then checks to see if the person’s orientation has changed in a set range within 0.5s, which would indicate a person has fallen or toppled over. If the person’s orientation has changed, the algorithm then examines to see if that orientation remains after 10s, which would indicate the person is immobilized in their fallen position on the ground. If this holds true, the algorithm recognizes this as a fall. A failure of any of the intermediate decision conditions would reset the triggers and send you back to the start. The strength of this algorithm is that it requires an activity to break two AM thresholds and have an orientation change. Ideally this additional lower threshold would reduce the number of false positives.

## Slide 12: Methodology
START
Collectiong data from ADXL335
Calculate acceleration magnitude
(AM)
AM breaks lower threshold?
AM breaks upper threshold within .5s
orientation change in range within .5s
Orientation remains after 10s?
Fall detected & trigger GSM
across x,y and z axis sensed by accelerometer.

## Slide 13: Methodology
B.Tech Electronics and Communication Engineering – Final Review Presentation - SENSE
Tabular representation of Upper and lower peak values of acceleration(g) during various ADL(activities in daily living)

## Slide 14: Methodology
B.Tech Electronics and Communication Engineering – Final Review Presentation - SENSE
Graph showing the upper fall threshold and lower fall threshold reach during a fall. It is plotted
In accordance with resultant acceleration(g)v/s time

## Slide 15: Results and Discussion
B.Tech Electronics and Communication Engineering – Final Review Presentation - SENSE
Hardware Setup
The project is build with Arduino uno used as a microcontroller to control the sensors(pulse , accelerometer) and modules(GPS, GSM) and execute such that it provides desired results.
This setup has to be attached to waist /chest and pulse sensor attached to finger of the user.
Two cases of results scenarios are possible using this model, they are explained in detail

## Slide 16: Results and Discussion
B.Tech Electronics and Communication Engineering – Final Review Presentation - SENSE
Scenario 1
Scenario 1:
When the fall is automatically detected by the working model,
It sents a message to caretaker informing about the fall detected and the pulse rate at the time of fall along with the latitude and longitude location of the victim who has fallen and need immediate assistance.

## Slide 17: Results and Discussion
B.Tech Electronics and Communication Engineering – Final Review Presentation - SENSE
Scenario 2
Scenario 2:
When the person itself feels unwell and is in need of assistance, he has a provision to press panic button which sents response to caretaker along with heart rate and location of the user .

## Slide 18: Conclusions
The results of the project is satisfactory with desired output of fall detection of a person.
The output comprises of an SMS to caretaker confirming the fall detection, along with the pulse rate during that fall and the latitude and longitude location of the victim.
The pulse rate value is an advantage if it is abnormal then we can make sure the situation of the user is bad and can take immediate action to help that person.
There is also a panic push button, in case of emergency ,the user can press and notify the caretaker that he is not well and require assistance.

## Slide 19: Future Directions of the Work
This project is a prototype design. however if you can include two more accelerometer to be attached in thighs ,you can also monitor the sleep cycle of the person.
The prototype can be implemented in real time using advanced technology by means of Smartphones.
Latest Smartphones have built in accelerometer sensor (motion sensor), GPS and GSM and certain phones even has pulse sensor.
Hence , an application can be developed on Android/Apple Appstore which can work similar to this project.

## Slide 20: References
[1] World Health Organisation. Global report on falls prevention in older age. World Health Organisation,2007.
[http://www.who.int/ageing/publications] Falls_prevention7March.pdf]
[2] Bergland, A., and TB Wyller. "Risk factors for serious fall related injury in elderly women living at home." Injury Prevention (2004): doi:10.1136/ip.2003.004721.
[3] Yardley, Lucy, and Helen Smith. "A Prospective Study of the Relationship Between Feared Consequences of Falling and Avoidance of Activity in Community-Living Older People." Gerontologist (2002) .
[4] Tinetti, M. E., M. Speechley, and S. F. Ginter. "Risk factors for falls among elderly persons living in the community." (1989)
SENSE- ECE499 - Capstone Project - Final Viva-Voce Presentation

## Slide 21: References
[5] Bueno-Cavanillas, A., F. Padilla-Ruiz, J. J. Jiménez-Moleón, C. A. Peinado-Alonso, and R. Gálvez-Vargas. "Risk Factors in Falls Among the Elderly According to Extrinsic and Intrinsic Precipitating Causes." European Journal of Epidemiology, 2000. doi:10.1023/A:1007636531965.
[6] Rafael Luque, Gema Redondo , María-José Morón , and Eduardo Casilari. "Comparison and Characterization of Android-Based Fall Detection Systems." Sensorsdoi:10.3390/s141018543.
[7] Bourke, A. K., J. V. O’Brien, and G. M. Lyons. "Evaluation of a threshold-based tri-axial accelerometer fall detection algorithm." Gait & Posture (2007): doi:10.1016/j.gaitpost.2006.09.012
SENSE- ECE499 - Capstone Project - Final Viva-Voce Presentation

## Slide 22: Acknowledgements
VIT Management
HOD
Parents
Internal and External Guides
Staff members